Myron PIV

Dual Q-Switched Diode-pumped  Nd:YAG Lasers

F E A T U RES

  Flexible configuration for combined and independent laser operations

  No DI water requirement

  Field-proven long-life diode module

  Rugged design, high relia- bility

  Up to 20 KHz operating rep- etition rate

  Average output up to 60 W

  Multi-mode and TEM00 mode output

  Smooth beam profile at fo- cus

  Ideal for Particle Image Ve- locimetry and Industrial ap- plications

AP PL IC AT IO NS

  PIV

  Ultrafast pumping

  Material processing

  Micromachining

The Myron PIV combines two independ- ent diode-pumped, Q-switched second harmonic Nd;YAG lasers into one laser beam. It features a field-proven long-life diode module and no DI water require- ment for water chiller. The rugged enclo- sure design, optimized cavity design and PRF adjustment result in excellent output stability  over  a  large  dynamic  range  as well as increased reliability for long-term operation. The Myron PIV is available in both TEM00 and Multi-mode output. The two laser head design makes the PIV sys- tem flexible in combined and separated laser applications to provide one high- powered or two synchronized half- powered laser outputs. In either case, the two  laser  beams  can  be  synchronized with the adjustable beam delay.

Two Myron lasers are identical in optical design giving temporally and spatially matched laser pulses for the highest cross-correlation performance. Each la- ser  can  be  independently  triggered  via TTL pulses. The external beam combina- tion allows easier access to optical com- ponents and more flexible laser applica- tions.

The Myron PIV provides an optimum so- lutions for scientific as well as industrial customers for applications, such as PIV, ultrafast amplifier pumping, material pro- cessing, micromachining, etc.

Myron PIV-60-M Green

Myron PIV-40-0

Green

Myron PIV-60-M IR

Myron PIV-40-0

IR

| Average Power | >58 W @ 10KHz > 38W @ 10 KHz >60 W @ 10KHz > 40W @ 10 KHz |
| --- | --- |
| Repetition Rate | 4- 20 KHz 4-20 KHz 4-20 KHz 4-20 KHz |
| Wavelength | 532 nm 532 nm 1064 nm 1064 nm |
| Pulse width | <120 ns <90 ns <120 ns <90 ns |
| Spatial Mode | M2 <10 M2 <1.2 (TEM00) M2 <10 M2 <1.2 (TEM00) |
| Beam Size (1/e2) | ~ 1 mm ~ 1 mm ~ 1 mm ~ 1 mm |
| Energy Stability | <2 % RMS <2 % RMS <2 % RMS <2 % RMS |
| Polarization | Cross Cross Cross Cross |